## Slide 1: Parallax Propeller
by Kyle Kurzhal

## Slide 2: Background/Contributions
Parallax Inc. was founded in 1987 by Chip Gracey and Lance Walley
In 1992, Parallax created the BASIC Stamp 1 (great for learning and hobbyists)
Then, based on the BASIC Stamp model, the Propeller microcontroller was developed in 2006
Parallax has been greatly involved in electronics education
Stamps in Class program in 1997
Released source code of executable portions of ROM (2008)
Parallax Propeller 1 released as open source hardware under the GNU v3.0 (2014)

## Slide 3: General Facts/Unusual Features
Up to 80 MHz with low power usage
8 processors, each called a “Cog”
  Up to 20 MIPS
  Independent from other Cogs, allowing parallelization
Centrally shared memory, called the “Hub”
  Contains RAM/ROM
  Mutually exclusive – only accessible in round-robin fashion to each Cog for two cycles
  Runs at half the system clock speed
Timing of instruction executions is extremely important

## Slide 4: Memory Specifications
Cog RAM/registers
  2 KB each
  Long addressable
  Addresses $000-$1FF
Main/Hub RAM/ROM
  32 KB apiece
  Byte (8-bit), Word (2-byte), Long (2-word) addressable
  Addresses $0000-$7FFF (RAM) and $8000-$BFFF (ROM)
  ROM contains character definitions, Log and Anti-Log tables, a Sine table, a boot loader, and the Spin interpreter
Data stored in Little Endian format

## Slide 5: Registers
512, 32-bit registers per Cog
496 general purpose registers (addresses $000-$1EF)
16 special purpose registers (addresses $1F0-$1FF)
Registers are also considered to be RAM
May store entire instructions, data values, or addresses

## Slide 6: Data Types
Binary (denoted with a beginning “%”)
Quaternary (denoted with a beginning “%%”)
Decimal integers
Decimal floating-points (denoted with “e” for scientific notation or with “.” for decimals)
Hexadecimal (denoted with a beginning “$”)
Characters

## Slide 7: Instruction Set
RISC-based architecture
Two main languages
  Spin (interpreted from Hub RAM)
  Propeller Assembly (stored directly in Cog registers)
Instructions
  Logic
  Arithmetic
  Control
  I/O
  Hub

## Slide 8: Instruction Format
32-bit instructions
Spin
  Interpreter stored in registers
  Execution instructions fetched from Hub RAM
Propeller Assembly
  Instruction - bits 31-26
  Effects (flags) - bits 25-22
  Execution condition (If statement) - bits 21-18
  Destination register - bits 17-9
  Source register or 9-bit immediate value - bits 8-0

## Slide 9: Addressing Modes
Spin
  Direct addressing
  Indirect addressing
  Indexed addressing for special purpose register array (SPR)
  A form of base-relative addressing for certain instructions
Propeller Assembly
  Direct addressing
  Indirect addressing
  Immediate addressing – denoted by '#' in source register

## Slide 10: I/O
32 I/O pins
  28 general purpose
  4 special purpose (until after boot-up)
  May be simultaneously accessible
Direction register – controls if a pin is considered output and if the associated Cog may output to it.
INA register – input register
OUTA register – output register
Dependent upon the programmer

## Slide 11: Electronic Resources
http://www.parallax.com/company/about-us
http://forums.parallax.com/showthread.php/101483-Propeller-ROM-source-code-HERE>
http://forums.parallax.com/showthread.php/135599-Converting-bytes-to-Strings
http://hackaday.com/2014/08/07/parallax-propeller-1-goes-open-source/
http://www.tceaconvention.org/2014/handouts/Proposal141400.pdf
http://www.parallax.com/sites/default/files/downloads/P8X32A-Web-PropellerManual-v1.2_0.pdf
http://www.parallax.com/sites/default/files/downloads/P8X32A-Propeller-Datasheet-v1.4.0_0.pdf
http://makezine.com/2014/08/06/parallaxs-propeller-1-silicon-goes-open-source/>.

## Slide 12: Github
Presentation document and slideshow at:
https://github.com/kkurzhal/CS_311